## Slide 1: The OU-ISIR Gait database Comprising the Large Population Dataset and Performance Evaluation of Gait Recognition

## Slide 2: Introduction
Gait-based biometrics at a distance
  Application to wide-area surveillance
Finger
print
Iris
DNA
Face
Distance from a sensor
Near
Far
Precision
High
Low
Gait database is essential for the development of gait-based biometrics
Gait

## Slide 3: Related work
Existing major gait database
CASIA
Yu et al. 2006
USF
Sarkar et al. 2005
OU-ISIR Treadmill
Mori et al. 2010
Mannami et al. 2010
Large population
Okumura et al. 2010
Makihara et al. 2011
Soton
Nixon et al. 2001
Number and diversity of subjects
Small
Large
Variation in walking conditions
Large
Small
At most 185 subjects
Genders and ages are biased
Performance evaluation with statistical reliability
Evaluation of the robustness
Number and diversity of subjects
Camera pose variations introduce
bias into the evaluation results

## Slide 4: Objective
Construction of the world’s largest gait database
  Focus on “Number and diversity of subjects”
Investigation of the upper limit of gait-recognition performance in statistically reliable way
Study on the difference of gait-recognition performance between genders and age groups

## Slide 5: Proposed dataset
“The OU-ISIR Gait Database, Large Population Dataset” (OU-LP)
  Major upgrade of previous works
    1,035 subjects in Okumura et al. 2010
    1,728 subjects in Makihara et al. 2011
Extensions from the previous works
  Number of subjects : 4,007
    2,135 males and 1,872 females with age ranging 1 to 94 year old
  All silhouette images are normalized
    Biases of camera rotation are removed
  Observation angles of subjects are specifically defined
    Previous work merely defined as “side view”
Statistically reliable evaluation
More equitable evaluation
Fair analysis in terms of the observation angles

## Slide 6: Capturing system
3 m (approx.)
3 m (approx.)
4 m
Capture interval
Start
Green panel
Acceleration section
Deceleration section
Camera 2
Camera 1
End
Walking course
Green carpet
4 m (approx.)
Point Grey research Flea2
Image size
  VGA (640 by 480 pixel)
Frame-rate
  30 fps
Camera 1

## Slide 7: Data collection
In conjunction with demonstration in five exhibitions
Each subject
  Signed release agreement for research-purpose use
  Provided gender and age information
Exhibition | Term | #Days | #Visitors (approx.)
Outreach activity in DIM (Dive Into the Movie) project | March 2009 | 3 | 1,600
5th Regional Disaster and Crime Prevention Expo | June 2010 | 2 | 280
Open campus at Osaka university 2010 | Aug 2010 | 1 | 70
Open campus at Osaka university 2011 | Aug 2011 | 1 | 90
Outreach activity in CREST project | Aug 2011 | 5 | 2,000

## Slide 8: Statistics of OU-LP
Number of subjects : 4,007 (2,135 males and 1,872 females)
Distributions of subject’s gender and age
Examples

## Slide 9: Subsets of OU-LP
Two primal subsets
  2 sequences/subject : OU-LP-A
  1 sequence/subject : OU-LP-B
Evaluation of recognition performance
Investigation of gender/age estimation

## Slide 10: Subsets of OU-LP
Two primal subsets
  2 sequences/subject : OU-LP-A
  1 sequence/subject : OU-LP-B
Further subsets based on observation angle
X
Y
Camera center
: Subject
: Observation angle
Walking direction
Surface of wall (green panel)
: Line of sight
Z
A section of 55 [deg]-centered gait period
A section of 65 [deg]-centered gait period
A section of 75 [deg]-centered gait period
A section of 85 [deg]-centered gait period
Evaluation of recognition performance
Investigation of gender/age estimation

## Slide 11: Subsets of OU-LP
Two primal subsets
  2 sequences/subject : OU-LP-A
  1 sequence/subject : OU-LP-B
Further subsets based on observation angle
  Number of subjects
Primal subset | Observation angle |  |  |  |  | Total
 | 55 [deg] | 65 [deg] | 75 [deg] | 85 [deg] | All | 
A | 3,706 | 3,770 | 3,751 | 3,249 | 3,141 | 3,835
B | 3,998 | 4,005 | 4,002 | 3,923 | 3,904 | 4,007
A/B-55
A/B-65
A/B-75
A/B-85
A/B-All
Evaluation of recognition performance
Investigation of gender/age estimation

## Slide 12: Advantages
Large population
  4,007 subjects in total
  Approx. 20 times more than the existing public gait database
Whole generation
  Age range from 1 to 94 yrs
  Each 10-year intervals contains over 400 subjects (from 5 to 49 yrs)
Gender balance
  Male : Female = 1.1 : 1
Silhouette quality
  All the silhouette images are visually checked at least twice and manually modified if necessary

## Slide 13: Preprocessing Silhouette extraction
Original sequence
Silhouette sequence
Manual denoising if necessary
Background subtraction
Camera-pose variation
Direct use introduces some biases in evaluation results

## Slide 14: Preprocessing Correction of camera rotation
X
Z
Y
Image plane
Camera coordinate system
z
x
y
Subject
X
Z
Y
Image plane
Camera coordinate system
z
x
y
Subject
Original captured image
Distortion corrected image
Rotation corrected image
[Tsuji et al. 1985]
Vertical center of image
Rotation correction by using vanishing points

## Slide 15: Preprocessing Creation of size-normalized silhouette
Original sequence
Silhouette sequence
Background subtraction
Rotation correction
Size-normalized silhouette sequence
88 x 128 pixel
Registration and size-normalization

## Slide 16: Gait recognition approach
Period detection
t
P
Gait period detection
Gait feature creation : appearance and period-based features
Gait Energy Image (GEI)
Frequency Domain Feature (FDF)
Gait Entropy Image (GEnI)
Gait Flow Image (GFI)
Chrono-Gait Image (CGI)
Masked GEI (MGEI)
Gait feature matching
Probe
Gallery
Direct matching
Dissimilarity is measured by L2 norm
Han and Bhanu 2006
Makihara et al. 2006
Lam et al. 2011
Wang et al. 2010
Bashir et al. 2009
Bashir et al. 2010

## Slide 17: Experiments
Performance evaluation of gait recognition
  1. Effect of number of subjects
  2. Comparison of gait feature
  3. Effects of gender and age

## Slide 18: Performance evaluation of gait recognition Effect of number of subjects
Data set: OP-LP-A-65 (3,770 subjects)
Reliability comparison: Whole set vs. Subset (100 subjects)
Gait feature: GEI
Estimated standard deviation
: observed FRR
: #subjects
Gray bar: observed deviation in 100 different subsets
ROC curve
[Snedecor and Cochran 1967]

## Slide 19: Performance evaluation of gait recognition Gait feature comparison
Data set: OP-LP-A-All (3,141 subjects)
  ※ Performance older was almost
  independent of the observation angle
GEI ≈ FDF > CGI ≈ GEnI > GFI > MGEI
  Performance order
ROC curve
CMC curve
  Better performance
  Better performance
GEI
FDF
CGI
GFI
GEnI
MGEI

## Slide 20: Performance evaluation of gait recognition Effects of gender and age
Data set: OP-LP-A-65 (3,770 subjects)
Gait feature: GEI
Performance comparison between gender/age groups
  Number of subjects
5-year interval
10-year interval

## Slide 21: Performance evaluation of gait recognition Effects of gender
Equal Error Rate (EER) among genders and age groups
  Better performance
Performance
Female > Male
  Dissimilarity distribution
  Dissimilarity distribution
Intra-subject variations: Female ≈ Male
Inter-subject variations: Female > Male
Intra
Inter

## Slide 22: Performance evaluation of gait recognition Effects of age
Equal Error Rate (EER) among genders and age groups
  Better performance
Gradual improvement
  Dissimilarity distribution of the same subjects
  Male
  Female
  Dissimilarity
  Dissimilarity
  Age
  Age
Gait fluctuation is small
 Adults have fixed gait pattern
Immaturity of children’s walking causes large intra-subject gait fluctuation

## Slide 23: Performance evaluation of gait recognition Effects of age
Equal Error Rate (EER) among genders and age groups
  Better performance
Gradual improvement
  Dissimilarity distribution of the same subjects
  Male
  Female
  Dissimilarity
  Dissimilarity
  Age
  Age

## Slide 24: Conclusion and future work
Conclusion
  We constructed the world’s largest gait database
    The number of subjects: 4,007
    Age range: 1 to 94 yrs
  Gait-recognition performance is evaluated with statistically reliability
    Comparison of state-of-the-art gait representation
    Study on the performance difference between genders and age groups
Future work
  Data collection of very young child and elderly